## Slide 1: LOGICAL SHIFT
In a logical shift the serial input to the shift is a 0.
A right logical shift operation:
A left logical shift operation:
In a Register Transfer Language, the following notation is used
  shl for a logical shift left
  shr for a logical shift right
  Examples:
    R2  shr R2
    R3  shl R3
0
0
For simplicity we assume that register symbols are same on both sides of arrow, but it is not necessary
1
0
0
1
1
0
1
1
0
1
0
0
1
1
0
1
1
0

## Slide 2: CIRCULAR SHIFT
In a circular shift the serial input is the bit that is shifted out of the other end of the register.
A right circular shift operation:
A left circular shift operation:
In a RTL, the following notation is used
  cil for a circular shift left
  cir for a circular shift right
  Examples:
    R2  cir R2
    R3  cil R3
1
0
0
1
1
0
1
1
1
0
0
1
1
0
1
1

## Slide 3: ARITHMETIC SHIFT
An arithmetic shift is meant for signed binary numbers (integer)
The main distinction of an arithmetic shift is that it must keep the sign of the number same while performs the right or left shift.
A right arithmetic shift operation:
A left arithmetic shift operation:
sign
bit
0
sign
bit
1
0
1
0
0
1
1
1
1
1
1
0
0
1
1
1
1
0